File ID: ESRE025A.doc

IMPLEMENTATION OF LOCAL COMPETITION

CRTC INTERCONNECTION STEERING COMMITTEE

Report to the CRTC

by

INDUSTRY WORKING GROUP

Emergency Services (9-1-1) Working Group (“ESWG”)

TIF25

Consensus Report

TITLE:	Wireless CLEC: Ontario CLEC-Municipality 9-1-1 Service Agreement

DATE:	25 April 2002

IMPLEMENTATION OF LOCAL COMPETITION

Consensus Report to the CRTC

Task ID(s):	ESTF025

Task Name(s): 	Wireless CLEC: Ontario CLEC-Municipality 9-1-1 Service Agreement

Task Description(s):

To amend the model Agreement for the Provision of 9-1-1 Emergency Calling Service in the Province of Ontario (reference ESWG Report ESRE006E) as required to accommodate wireless CLECs, consistent with Orders CRTC 2000-830 and 2000-831.

Conclusions:

The ESWG has reached consensus on a model Agreement for the Provision of 9-1-1 Emergency Calling Service in the Province of Ontario – For Use by Wireless Competitive Local Exchange Carriers.

This agreement has been expressly drafted to apply uniquely in areas where the wireless CLEC has deployed wireless E9-1-1, defined as the capability to display at a PSAP, in real time while a wireless 9-1-1 call is in progress, the caller’s 10-digit call-back number as well as the address/location of the cell site/sector that captured the call.

Recommendations:

The ESWG recommends that the Commission adopt the model agreement.

Further Activities:

Work with respect to other provinces will be initiated as required.

Attachments:

Agreement for the Provision of 9-1-1 Emergency Calling Service in the Province of Ontario – For Use by Wireless Competitive Local Exchange Carriers – with revision marks to indicate changes relative to the model agreement included in ESWG Report ESRE006E

Agreement for the Provision of 9-1-1 Emergency Calling Service in the Province of Ontario – For Use by Wireless Competitive Local Exchange Carriers – clean version without revision marks

Version 25-04-2002

AGREEMENT FOR THE PROVISION OF

E9-1-1 EMERGENCY CALLING SERVICE IN PROVINCE OF ONTARIO

- FOR USE BY WIRELESS COMPETITIVE LOCAL EXCHANGE CARRIERS

BETWEEN:	___________________________________

(hereinafter called the “Municipality”)

AND:	The Wireless Competitive Local Exchange Carrier identified as such

in Schedule “A” to this Agreement

(hereinafter called the “Wireless CLEC”)

WHEREAS the Municipality provides access to emergency services via a Provincial Emergency Reporting System (“PERS”), an enhanced 9-1-1 service; and

WHEREAS the Wireless CLEC wishes to operate in the Municipality as a CLEC, or otherwise wishes to provide wireless telecommunications service in the Municipality with a grade of 9-1-1 service equivalent to that of a CLEC; and

WHEREAS the Wireless CLEC has entered into an interconnection agreement for the provision of E9-1-1 service with the Incumbent Local Exchange Carrier (“ILEC”),

NOW THEREFORE, in consideration of the premises and the mutual promises contained herein the parties hereto agree as follows:

1.	Definitions:

For the purposes of this Agreement, the following terms have the meanings defined below:

1.1	“ALI”:	Automatic Local Identification

In the case of wireless telecommunications services, refers to a database feature that displays to PSAP's and ERA's address/location data with respect to the Cell Site/Sector that captured the 9-1-1 call.

1.2	“Call Answer”:

The act of answering E9-1-1 calls, determining the type of ERA required and directing the E9-1-1 call to that ERA.

1.3	“CBN”:	Call Back Number

The E9-1-1 system’s capability to automatically identify the 10-digit calling telephone number and to provide a display of that number at PSAP’s and ERA’s.

1.4	“Cell Site/Sector”:

An element of wireless network infrastructure at which wireless telecommunications signals are received and transmitted, most often associated with a tower structure.  At any given tower structure (or equivalent infrastructure location), a single network element may be installed to operate omni-directionally, in which case one refers to a Cell Site, or multiple network elements may be installed to each operate in a particular cardinal direction, in which case one refers to multiple Cell Sectors.

1.5	“Commission”:

The Canadian Radio-television and Telecommunications Commission (CRTC), and its successors.

1.6	"E9-1-1 Emergency Calling Service"

The ILEC/Wireless CLEC service that provides the end user subscriber with the universally recogonized E9-1-1 three-digit dial access to ERA's serving their communities.

1.7	“E9-1-1 Service Provider”:

The ILEC that provides an E9-1-1 service to the Municipality, pursuant to a tariff and/or agreement through which access to E9-1-1 emergency calling is made available to the ILEC’s and Wireless CLEC’s end user subscribers located within the E9-1-1 Serving Area.

1.8	“ERA”: Emergency Response Agency

A communication centre open 24 hours a day, 365 days a year to which emergency calls are transferred from the PSAP and which is the agency responsible for dispatching emergency personnel (emergency medical, fire or law enforcement).

1.9	"ESRD": Emergency Service Routing Digits

A network-based 10-digit routable, non-dialable, telephone number used by a Wireless CLEC to uniquely identify a Cell Site/Sector.  The ESRD is used by the 9-1-1 service to route the call to the designated PSAP.  The ESRD must be unique and cannot be a telephone number assigned to an end user subscriber.

1.10	“ESZ”: Emergency Service Zone

A defined area consisting of a specific combination of Municipality, law enforcement, fire, emergency medical and PSAP coverage areas.

1.11	“Exchange Services”:

Any local telecommunications service offered by a Wireless CLEC, providing service as a CLEC, to its end user subscribers, either directly or indirectly through a Wireless CLEC authorized reseller.

1.12	“Local Subscriber”:

A Wireless CLEC end user subscriber whose telephone number is from a central office code associated with a CLEC network point of interconnection located within the Municipality’s boundaries, and who subscribes to any of the Wireless CLEC’s Exchange Services.

1.13	“PSAP”: Public Safety Answering Point

A communications facility open 24 hours a day, 365 days a year, and responsible for answering, redirecting or transferring emergency calls to ERA’s.  The PSAP is the first point of reception for all E9-1-1 calls in its serving area.

1.14	“SAG”: Street Address Guide: E9-1-1 Street Address Database

The database operated by the Wireless CLEC that contains Cell Site/Sector addresses, ESRDs and other data required for the management of ALI..

1.15	“Serving Area”:

The area within the Municipality’s boundaries, as determined by the Municipality, from which E9-1-1 calls will be directed to a particular PSAP.

2.	Service Description

2.1	E9-1-1 Emergency Calling Service is provided to the Wireless CLEC end user subscribers (Local Subscribers and roaming subscribers) connected to the Wireless CLEC network.  The service provides for the transport of 9-1-1 dialled calls through the E9-1-1 Service Provider to the PSAP and other ERA’s.

2.2	The Wireless CLEC provides its end user subscribers with three digit dial access to the E9-1-1 Service from each of its central offices to provide service coverage specified by the Municipality.  Answering of the call and the emergency response is the responsibility of the Municipality and is not provided by the Wireless CLEC as part of E9-1-1 Emergency Calling Service.

2.3	The E9-1-1 call is delivered to a PSAP operated by the Municipality.  The attendant at the PSAP determines the nature of the emergency and forwards the call to the appropriate ERA. The answering attendants at the ERA’s are supported by the following special features provided by the E9-1-1 Service Provider:

i)	Selective Routing and Transfer:

A feature that automatically routes an E9-1-1 call to the appropriate PSAP and transfers the E9-1-1 call to the appropriate ERA based upon the ESRD of the Cell Site/Sector which captured the call.

ii)	Maintenance of ALI

The E9-1-1 Service Provider maintains the ALI database.

iii)	Integrity Check

This allows the ERA to verify that the E9-1-1 access lines to its bureau are in working order.

The operation of the Selective Routing and Transfer and ALI features is dependent upon the accuracy of the Wireless CLEC records and information received from the Municipality and others, such as, new street information and boundary changes.

3.	Object

3.1	In accordance with the terms and conditions of this Agreement, the Municipality and the Wireless CLEC agree to fulfil their respective obligations under this Agreement in order to make available an E9-1-1 emergency calling service to Wireless CLEC end user subscribers.

4.	Conditions of Service

4.1	As conditions of providing E9-1-1, the Wireless CLEC agrees to:

4.1.1	Make E9-1-1 accessible to all of its Local Subscribers when they are physically in the Serving Area, as well as to any roaming end users who may be on the Wireless CLEC’s network in the Serving Area.  Roaming end users may include the Wireless CLEC’s end users from its other wireless service territories, as well as end users of the Wireless CLEC’s domestic and international roaming partners.

4.1.2	Provide E9-1-1 through the network of the E9-1-1 Service Provider under the terms and conditions of an Interconnection Agreement between the ILEC and the Wireless CLEC, to the PSAP.

4.1.3	Provide CBN/ESRD/ALI data, and other data to the E9-1-1 Service Provider which, in turn, shall provide such data to the PSAP and ERA as deemed appropriate to the Municipality, Wireless CLEC's and ILEC.

4.1.4	Provide a telephone number to the PSAP that is accessible 24 hours a day and seven days a week, for the reporting of troubles.

4.1.5	Maintain and update the SAG subject to receipt of the information required to be provided by the Municipality pursuant to this Agreement.

4.1.6	Provide a facsimile telephone number or alternate address (eg: e-mail), where incorrect Cell Site/Sector information can be sent by the PSAP for corrections.

4.2	As conditions of obtaining E9-1-1 PERS, the Municipality shall:

4.2.1	Provide and operate a PSAP for the Serving Area on a 24 hour-per-day, 365 day-per-year basis.  Answering and handling of emergency calls, along with the emergency response, is the responsibility of the Municipality and is not part of Wireless CLEC E9-1-1 Emergency Calling Service.

4.2.2	Provide, operate and manage the personnel and the equipment, including terminal equipment, required to receive and process all E9-1-1 emergency calls directed to the PSAP.

4.2.3	Co-ordinate participation of all ERA’s in the Serving Area with respect to

E9-1-1 PERS.  This will include:

4.2.3.1	Ensuring the involvement of the ERA’s;

4.2.3.2	Determining the Serving Areas and ESZ’s served by the PSAP and ERA’s;

4.2.3.3	Providing and validating, as reasonably required by the Wireless CLEC, the geographical information necessary to determine the most appropriate ESZ to assign to each Cell Site/Sector coverage area, including providing maps of ESZ boundaries where available, and otherwise helping to associate Cell Site/Sector addresses with ESZs;

4.2.3.4	Informing the Wireless CLEC immediately of all changes that may occur in that same geographical information, including street names, and addresses; and

4.2.3.5	Provide a 24 hour a day, seven days a week telephone number that will be available to the Wireless CLEC for the reporting of troubles or information.

4.2.4	Provide access to fire, law enforcement and emergency medical services within the Municipality, and provide the address, contact, telephone and facsimile numbers of these services to the Wireless CLEC’s.

4.2.5	Provide the Wireless CLEC’s with a minimum of ninety (90) days written notice of an intended change in the location of the PSAP and the borders of the Serving Areas or the ESZ’s.

4.3	The Municipality may contract with a third party for the management and operation of the PSAP, but in such event, the Municipality shall remain responsible for all aspects of the operation of the PSAP and shall not be relieved of any of its obligations under this Agreement. The locations of the PSAP and ERA’s are described in Schedules “B” and “D”.

5.	Characteristics of E9-1-1 PERS

5.1	The E9-1-1 PERS permits the utilization of CBN/ESRD/ALI and Selective Routing and Transfer features.  The availability and reliability of these features depends on the following:

5.1.1	The terminal systems and the operating mode selected for the PSAP and ERA’s;

5.1.2	The type of Exchange Service and the equipment and/or telephone systems from which E9-1-1 calls originate;

5.1.3	The accuracy of the data, which itself is dependent upon the information provided by various sources, (for example, Wireless CLEC’s, the Municipality, the E9-1- 1 Service Provider, other telecommunication carriers...); and

5.1.4	The characteristics and reliability of the E9-1-1 service provided by the E9-1-1 Service Provider to the extent that the Wireless CLEC’s participation in the provision of E9-1-1 Emergency Calling Service is dependent on the E9-1-1 service provided by the E9-1-1 Service Provider.

6.	Confidential Information

6.1	The Wireless CLEC provides to the E9-1-1 Service Provider which, in turn, provides to the Municipality on a call-by-call basis the telephone number of the end user subscriber who placed the 9-1-1 call and the location of the Cell Site/Sector that captured the E9-1-1 call.  The information, if confidential as identified in Article 6.2, is provided to the E9-1-1 Service Provider which, in turn, is provided to the Municipality on a confidential basis, for the sole purpose of responding to E9-1-1 emergency calls.

6.2	The information consisting of telephone numbers of the end user subscribers whose listings are not published in directories or listed in the E9-1-1 Service Provider’s Directory Assistance records is confidential.  The individual calling E9-1-1 waives the right to privacy to the extent that the telephone number and physical location of the Cell Site/Sector that captured the E9-1-1 call are furnished to the Municipality.

6.3	Any information including all written documentation provided by the Wireless CLEC to the Municipality, its employees, servants, agents, assigns and/or contractors pertaining to the design, development, implementation, the operation and the maintenance of E9-1-1 PERS is confidential and will be provided only to such persons who have a need to know for the purposes of this Agreement.  The Municipality will not permit any of its employees, servants, agents, assigns and/or contractors to duplicate, reproduce or otherwise copy any such confidential information for any purpose whatsoever, except as may be required by any such employees, servants, agents, assigns and/or contractors with a need to do so for the purposes of providing a E9-1-1 emergency calling service or except as may be required by law.

6.4	Confidential CBN/ESRD/ALI and associated information of the Wireless CLEC’s end user subscribers are provided to the PSAP and ERA’s as directed by the Municipality solely for the purpose of enabling the PSAP and ERA’s to verify the location from which the E9-1-1 call is placed.  The Municipality, the PSAP and the ERA's shall not use such information for any other purposes, except as may be required by law.

6.5	The Wireless CLEC and the Municipality shall abide by all applicable federal and provincial legislation with respect to the protection of privacy in effect from time to time.

7.	Quality of the Wireless CLEC E9-1-1 PERS

7.1	The Wireless CLEC agrees to interconnect to E9-1-1 in a manner that meets quality standards generally accepted in North America for such services, and in so doing shall have regard to the standards identified in the ILEC/Wireless CLEC Interconnection Agreement.

7.2	The Wireless CLEC shall use reasonable efforts to restore service as quickly as possible on a priority basis should there be any interruption, delay, mistake or defect in transmission or in its facilities.

8.	Quality of Municipality’s Service

The Municipality shall implement and ensure the operation of its PSAP in a manner that meets the quality standards generally accepted in North America for such services.

9.	Implementation Schedule

To the extent that E9-1-1 is not already in place prior to the Wireless CLEC becoming a CLEC, the Wireless CLEC and the Municipality agree that the implementation of E9-1-1 within the Serving Area will be carried out pursuant to an implementation schedule to be mutually agreed to by the Wireless CLEC, the Municipality and the E9-1-1 Service Provider in writing and which may be changed from time to time by agreement of the parties.

10.	Limitation of Liability

10.1	Except with regard to physical injuries, death or damage to property occasioned by its negligence, the Wireless CLEC’s liability for negligence is limited to $20.

10.2	Except with regard to physical injuries, death or damage to property occasioned by its negligence, the Municipality’s liability for negligence is limited to $20.

10.3 	The Municipality and the Wireless CLEC shall, during the term of this Agreement, maintain sufficient insurance to cover their respective obligations under this Agreement and shall provide evidence of same to the Wireless CLEC or the Municipality, as the case may be, on request.

11.	Term and Renewal

11.1	This Agreement shall be effective as of the date the Wireless CLEC executes Schedule “A” forming part of this Agreement, and shall expire on April 1, 2008.

11.2	The term of this agreement shall be automatically renewed for successive periods of five  (5) years after the initial term, as stipulated in Article 11.1.

11.3	The term of this Agreement and any renewal term shall be in force unless one party gives to the other at least six (6) months’ written notice of termination prior to the end of the said term.

11.4	Notwithstanding Article 11.1, this Agreement shall automatically terminate on the same date as:

- The E9-1-1 Service Provider ceases to provide an E 9-1-1 emergency calling service to the Municipality, or,

- The Wireless CLEC ceases to employ the E9-1-1 facilities of the E-9-1-1 Service Provider, in that it will provide its own E9-1-1 Emergency Calling Service.

12.	Force Majeure

12.1	Neither the Wireless CLEC nor the Municipality will be held responsible for any damages or delays as a result of war, invasion, insurrection, demonstrations, or as a result of decisions by civilian or military authorities, fire, floods, strikes, decisions or regulatory authorities, and, generally, as a result of any event that is beyond the Municipality’s or the Wireless CLEC’s reasonable control.

12.2	In the event of a disaster or force majeure, the Wireless CLEC and the Municipality will cooperate and make all reasonable efforts to provide temporary replacement service until permanent service is completely restored.

12.3	The Municipality may designate a back up Call Answer Centre to which E9-1-1 calls will be directed in the event that the primary PSAP is unable to accept the calls, for any reason.

12.4	The costs required to provide temporary replacement service will be borne according to the sharing of obligations between the Wireless CLEC and the Municipality, as indicated in Article 4 of this Agreement.

13.	Waiver

The failure of either party to require the performance of any obligation hereunder, or the waiver of any obligation in a specific instance, will not be interpreted as a general waiver of any of the obligations, hereunder, which will continue to remain in full force and effect.

14.	Relationship to the Parties

This Agreement will not create nor will it be interpreted as creating any association, partnership, any employment relationship or any agency relationship between the parties.

15.	Entire Agreement

15.1	Except as otherwise stated herein, this Agreement constitutes the entire agreement of the parties and supersedes any previous agreement, whether written or verbal.  Should any provision of this Agreement be declared null, void or inoperative, the remainder of the Agreement will remain in full force and effect.

15.2	The parties agree that Articles 1,6,10,12,14,15,16 and 17 of this Agreement shall survive and remain in force notwithstanding the expiration or termination of this Agreement.

15.3	It is expressly understood that this Agreement and E9-1-1 Emergency Calling Service are subject to such terms and conditions as the CRTC or its successors may impose from time to time.

16.	Arbitration Clause

Except with respect to any matter within the jurisdiction of the Commission, any dispute or disagreement that may occur pursuant to this Agreement will be settled in a binding manner by way of arbitration in accordance with the Arbitration Act, 1991 (Ontario), as amended.  Each party will bear its own costs of arbitration.  All decisions of the arbitrator(s) are fully binding and enforceable upon the parties.

17.	Notices

Any notice required pursuant to this Agreement shall be in writing and delivered personally, by courier, or sent by registered mail (with proper postage), to, in the case of notice to the Municipality, the address listed on this page, and in the case of the Wireless CLEC, the address listed in Schedule “A”, or to such other address as either party may indicate to the other.  In the event of a strike or other disruption of postal service, or an anticipated strike or disruption, delivery either personally or by courier only, will be effective.

Notice to the Municipality:

_______________________

_______________________

_______________________

_______________________

18.	 Applicable Law

This Agreement shall be governed by the laws of the Province of Ontario and Canada.

SIGNED, SEALED AND DELIVERED

THE MUNICIPALITY

Per: __________________________________

Per: __________________________________(c/s)

Dated: ________________________________

SCHEDULE “A”

Wireless CLEC Adherence Schedule

- This Schedule “A” forms part of an Agreement for the Provision of E9-1-1 Emergency Calling Service in the Province of Ontario - For Use by Wireless Competitive Local Exchange Carriers (the “Agreement”) between ____________________________ (“Municipality”), having executed the Agreement on _________________________, and the Wireless Competitive Local Exchange Carrier (the “Wireless CLEC”) identified below, having executed this Schedule “A” on ____________________________.

- Upon execution of this Schedule “A” and its delivery to the Municipality pursuant to the provisions of Article 17 of the Agreement, the Wireless CLEC agrees that it will be bound to the terms and conditions of the Agreement as if it had executed the Agreement directly.

- Pursuant to Article 17 of the Agreement, the Wireless CLEC’s address for notices is:

_______________________

_______________________

_______________________

_______________________

SIGNED, SEALED AND DELIVERED

WIRELESS CLEC:	__________________________________

Per: __________________________________

Per: __________________________________(c/s)

(I have the authority to bind the corporation)

SCHEDULE “B”

Location of PSAP and ERA’s

PSAP

Contact _____________________________________________________

Address _____________________________________________________

Phone _(_____)________________

Fax ___(_____)________________

Back-up PSAP

Contact ______________________________________________________

Address ______________________________________________________

Phone _(_____)_______________

Fax ___(_____)_______________

Fire: ERA Detail per Schedule D

Ambulance: ERA Detail per Schedule D

Police: ERA Detail per Schedule D

Municipal: Detail per Schedule C

SCHEDULE “C”

Municipal Contacts

911 Contact Information:

Main Municipal Contact: _____________________________________________

Address:

Street:              ______________________________________________________

Town/City       ______________________________________________________

Postal Code     _______________

Phone: _(______)________________

Fax: ___(______)________________

Municipal Address Co-ordinator: _______________________________________

Address:

Street:               ______________________________________________________

Town/City:       ______________________________________________________

Postal Code:     _________________

Phone: __(_____)__________________

Fax: ____(_____)__________________

SCHEDULE “D”

Serving Areas and Emergency Service Zones

Per attached Service Address Control Group documents.

Version 25-04-2002

AGREEMENT FOR THE PROVISION OF

E9-1-1 EMERGENCY CALLING SERVICE IN PROVINCE OF ONTARIO

- FOR USE BY WIRELESS COMPETITIVE LOCAL EXCHANGE CARRIERS

BETWEEN:	___________________________________

(hereinafter called the “Municipality”)

AND:	The Wireless Competitive Local Exchange Carrier identified as such

in Schedule “A” to this Agreement

(hereinafter called the “Wireless CLEC”)

WHEREAS the Municipality provides access to emergency services via a Provincial Emergency Reporting System (“PERS”), an enhanced 9-1-1 service; and

WHEREAS the Wireless CLEC wishes to operate in the Municipality as a CLEC, or otherwise wishes to provide wireless telecommunications service in the Municipality with a grade of 9-1-1 service equivalent to that of a CLEC; and

WHEREAS the Wireless CLEC has entered into an interconnection agreement for the provision of E9-1-1 service with the Incumbent Local Exchange Carrier (“ILEC”),

NOW THEREFORE, in consideration of the premises and the mutual promises contained herein the parties hereto agree as follows:

1.	Definitions:

For the purposes of this Agreement, the following terms have the meanings defined below:

1.1	“ALI”:	Automatic Local Identification

In the case of wireless telecommunications services, refers to a database feature that displays to PSAP's and ERA's address/location data with respect to the Cell Site/Sector that captured the 9-1-1 call.

1.2	“Call Answer”:

The act of answering E9-1-1 calls, determining the type of ERA required and directing the E9-1-1 call to that ERA.

1.3	“CBN”:	Call Back Number

The E9-1-1 system’s capability to automatically identify the 10-digit calling telephone number and to provide a display of that number at PSAP’s and ERA’s.

1.4	“Cell Site/Sector”:

An element of wireless network infrastructure at which wireless telecommunications signals are received and transmitted, most often associated with a tower structure.  At any given tower structure (or equivalent infrastructure location), a single network element may be installed to operate omni-directionally, in which case one refers to a Cell Site, or multiple network elements may be installed to each operate in a particular cardinal direction, in which case one refers to multiple Cell Sectors.

1.5	“Commission”:

The Canadian Radio-television and Telecommunications Commission (CRTC), and its successors.

1.6	"E9-1-1 Emergency Calling Service"

The ILEC/Wireless CLEC service that provides the end user subscriber with the universally recogonized E9-1-1 three-digit dial access to ERA's serving their communities.

1.7	“E9-1-1 Service Provider”:

The ILEC that provides an E9-1-1 service to the Municipality, pursuant to a tariff and/or agreement through which access to E9-1-1 emergency calling is made available to the ILEC’s and Wireless CLEC’s end user subscribers located within the E9-1-1 Serving Area.

1.8	“ERA”: Emergency Response Agency

A communication centre open 24 hours a day, 365 days a year to which emergency calls are transferred from the PSAP and which is the agency responsible for dispatching emergency personnel (emergency medical, fire or law enforcement).

1.9	"ESRD": Emergency Service Routing Digits

A network-based 10-digit routable, non-dialable, telephone number used by a Wireless CLEC to uniquely identify a Cell Site/Sector.  The ESRD is used by the 9-1-1 service to route the call to the designated PSAP.  The ESRD must be unique and cannot be a telephone number assigned to an end user subscriber.

1.10	“ESZ”: Emergency Service Zone

A defined area consisting of a specific combination of Municipality, law enforcement, fire, emergency medical and PSAP coverage areas.

1.11	“Exchange Services”:

Any local telecommunications service offered by a Wireless CLEC, providing service as a CLEC, to its end user subscribers, either directly or indirectly through a Wireless CLEC authorized reseller.

1.12	“Local Subscriber”:

A Wireless CLEC end user subscriber whose telephone number is from a central office code associated with a CLEC network point of interconnection located within the Municipality’s boundaries, and who subscribes to any of the Wireless CLEC’s Exchange Services.

1.13	“PSAP”: Public Safety Answering Point

A communications facility open 24 hours a day, 365 days a year, and responsible for answering, redirecting or transferring emergency calls to ERA’s.  The PSAP is the first point of reception for all E9-1-1 calls in its serving area.

1.14	“SAG”: Street Address Guide: E9-1-1 Street Address Database

The database operated by the Wireless CLEC that contains Cell Site/Sector addresses, ESRDs and other data required for the management of ALI..

1.15	“Serving Area”:

The area within the Municipality’s boundaries, as determined by the Municipality, from which E9-1-1 calls will be directed to a particular PSAP.

2.	Service Description

2.1	E9-1-1 Emergency Calling Service is provided to the Wireless CLEC end user subscribers (Local Subscribers and roaming subscribers) connected to the Wireless CLEC network.  The service provides for the transport of 9-1-1 dialled calls through the E9-1-1 Service Provider to the PSAP and other ERA’s.

2.2	The Wireless CLEC provides its end user subscribers with three digit dial access to the E9-1-1 Service from each of its central offices to provide service coverage specified by the Municipality.  Answering of the call and the emergency response is the responsibility of the Municipality and is not provided by the Wireless CLEC as part of E9-1-1 Emergency Calling Service.

2.3	The E9-1-1 call is delivered to a PSAP operated by the Municipality.  The attendant at the PSAP determines the nature of the emergency and forwards the call to the appropriate ERA. The answering attendants at the ERA’s are supported by the following special features provided by the E9-1-1 Service Provider:

i)	Selective Routing and Transfer:

A feature that automatically routes an E9-1-1 call to the appropriate PSAP and transfers the E9-1-1 call to the appropriate ERA based upon the ESRD of the Cell Site/Sector which captured the call.

ii)	Maintenance of ALI

The E9-1-1 Service Provider maintains the ALI database.

iii)	Integrity Check

This allows the ERA to verify that the E9-1-1 access lines to its bureau are in working order.

The operation of the Selective Routing and Transfer and ALI features is dependent upon the accuracy of the Wireless CLEC records and information received from the Municipality and others, such as, new street information and boundary changes.

3.	Object

3.1	In accordance with the terms and conditions of this Agreement, the Municipality and the Wireless CLEC agree to fulfil their respective obligations under this Agreement in order to make available an E9-1-1 emergency calling service to Wireless CLEC end user subscribers.

4.	Conditions of Service

4.1	As conditions of providing E9-1-1, the Wireless CLEC agrees to:

4.1.1	Make E9-1-1 accessible to all of its Local Subscribers when they are physically in the Serving Area, as well as to any roaming end users who may be on the Wireless CLEC’s network in the Serving Area.  Roaming end users may include the Wireless CLEC’s end users from its other wireless service territories, as well as end users of the Wireless CLEC’s domestic and international roaming partners.

4.1.2	Provide E9-1-1 through the network of the E9-1-1 Service Provider under the terms and conditions of an Interconnection Agreement between the ILEC and the Wireless CLEC, to the PSAP.

4.1.3	Provide CBN/ESRD/ALI data, and other data to the E9-1-1 Service Provider which, in turn, shall provide such data to the PSAP and ERA as deemed appropriate to the Municipality, Wireless CLEC's and ILEC.

4.1.4	Provide a telephone number to the PSAP that is accessible 24 hours a day and seven days a week, for the reporting of troubles.

4.1.5	Maintain and update the SAG subject to receipt of the information required to be provided by the Municipality pursuant to this Agreement.

4.1.6	Provide a facsimile telephone number or alternate address (eg: e-mail), where incorrect Cell Site/Sector information can be sent by the PSAP for corrections.

4.2	As conditions of obtaining E9-1-1 PERS, the Municipality shall:

4.2.1	Provide and operate a PSAP for the Serving Area on a 24 hour-per-day, 365 day-per-year basis.  Answering and handling of emergency calls, along with the emergency response, is the responsibility of the Municipality and is not part of Wireless CLEC E9-1-1 Emergency Calling Service.

4.2.2	Provide, operate and manage the personnel and the equipment, including terminal equipment, required to receive and process all E9-1-1 emergency calls directed to the PSAP.

4.2.3	Co-ordinate participation of all ERA’s in the Serving Area with respect to

E9-1-1 PERS.  This will include:

4.2.3.1	Ensuring the involvement of the ERA’s;

4.2.3.2	Determining the Serving Areas and ESZ’s served by the PSAP and ERA’s;

4.2.3.3	Providing and validating, as reasonably required by the Wireless CLEC, the geographical information necessary to determine the most appropriate ESZ to assign to each Cell Site/Sector coverage area, including providing maps of ESZ boundaries where available, and otherwise helping to associate Cell Site/Sector addresses with ESZs;

4.2.3.4	Informing the Wireless CLEC immediately of all changes that may occur in that same geographical information, including street names, and addresses; and

4.2.3.5	Provide a 24 hour a day, seven days a week telephone number that will be available to the Wireless CLEC for the reporting of troubles or information.

4.2.4	Provide access to fire, law enforcement and emergency medical services within the Municipality, and provide the address, contact, telephone and facsimile numbers of these services to the Wireless CLEC’s.

4.2.5	Provide the Wireless CLEC’s with a minimum of ninety (90) days written notice of an intended change in the location of the PSAP and the borders of the Serving Areas or the ESZ’s.

4.3	The Municipality may contract with a third party for the management and operation of the PSAP, but in such event, the Municipality shall remain responsible for all aspects of the operation of the PSAP and shall not be relieved of any of its obligations under this Agreement. The locations of the PSAP and ERA’s are described in Schedules “B” and “D”.

5.	Characteristics of E9-1-1 PERS

5.1	The E9-1-1 PERS permits the utilization of CBN/ESRD/ALI and Selective Routing and Transfer features.  The availability and reliability of these features depends on the following:

5.1.1	The terminal systems and the operating mode selected for the PSAP and ERA’s;

5.1.2	The type of Exchange Service and the equipment and/or telephone systems from which E9-1-1 calls originate;

5.1.3	The accuracy of the data, which itself is dependent upon the information provided by various sources, (for example, Wireless CLEC’s, the Municipality, the E9-1- 1 Service Provider, other telecommunication carriers...); and

5.1.4	The characteristics and reliability of the E9-1-1 service provided by the E9-1-1 Service Provider to the extent that the Wireless CLEC’s participation in the provision of E9-1-1 Emergency Calling Service is dependent on the E9-1-1 service provided by the E9-1-1 Service Provider.

6.	Confidential Information

6.1	The Wireless CLEC provides to the E9-1-1 Service Provider which, in turn, provides to the Municipality on a call-by-call basis the telephone number of the end user subscriber who placed the 9-1-1 call and the location of the Cell Site/Sector that captured the E9-1-1 call.  The information, if confidential as identified in Article 6.2, is provided to the E9-1-1 Service Provider which, in turn, is provided to the Municipality on a confidential basis, for the sole purpose of responding to E9-1-1 emergency calls.

6.2	The information consisting of telephone numbers of the end user subscribers whose listings are not published in directories or listed in the E9-1-1 Service Provider’s Directory Assistance records is confidential.  The individual calling E9-1-1 waives the right to privacy to the extent that the telephone number and physical location of the Cell Site/Sector that captured the E9-1-1 call are furnished to the Municipality.

6.3	Any information including all written documentation provided by the Wireless CLEC to the Municipality, its employees, servants, agents, assigns and/or contractors pertaining to the design, development, implementation, the operation and the maintenance of E9-1-1 PERS is confidential and will be provided only to such persons who have a need to know for the purposes of this Agreement.  The Municipality will not permit any of its employees, servants, agents, assigns and/or contractors to duplicate, reproduce or otherwise copy any such confidential information for any purpose whatsoever, except as may be required by any such employees, servants, agents, assigns and/or contractors with a need to do so for the purposes of providing a E9-1-1 emergency calling service or except as may be required by law.

6.4	Confidential CBN/ESRD/ALI and associated information of the Wireless CLEC’s end user subscribers are provided to the PSAP and ERA’s as directed by the Municipality solely for the purpose of enabling the PSAP and ERA’s to verify the location from which the E9-1-1 call is placed.  The Municipality, the PSAP and the ERA's shall not use such information for any other purposes, except as may be required by law.

6.5	The Wireless CLEC and the Municipality shall abide by all applicable federal and provincial legislation with respect to the protection of privacy in effect from time to time.

7.	Quality of the Wireless CLEC E9-1-1 PERS

7.1	The Wireless CLEC agrees to interconnect to E9-1-1 in a manner that meets quality standards generally accepted in North America for such services, and in so doing shall have regard to the standards identified in the ILEC/Wireless CLEC Interconnection Agreement.

7.2	The Wireless CLEC shall use reasonable efforts to restore service as quickly as possible on a priority basis should there be any interruption, delay, mistake or defect in transmission or in its facilities.

8.	Quality of Municipality’s Service

The Municipality shall implement and ensure the operation of its PSAP in a manner that meets the quality standards generally accepted in North America for such services.

9.	Implementation Schedule

To the extent that E9-1-1 is not already in place prior to the Wireless CLEC becoming a CLEC, the Wireless CLEC and the Municipality agree that the implementation of E9-1-1 within the Serving Area will be carried out pursuant to an implementation schedule to be mutually agreed to by the Wireless CLEC, the Municipality and the E9-1-1 Service Provider in writing and which may be changed from time to time by agreement of the parties.

10.	Limitation of Liability

10.1	Except with regard to physical injuries, death or damage to property occasioned by its negligence, the Wireless CLEC’s liability for negligence is limited to $20.

10.2	Except with regard to physical injuries, death or damage to property occasioned by its negligence, the Municipality’s liability for negligence is limited to $20.

10.3 	The Municipality and the Wireless CLEC shall, during the term of this Agreement, maintain sufficient insurance to cover their respective obligations under this Agreement and shall provide evidence of same to the Wireless CLEC or the Municipality, as the case may be, on request.

11.	Term and Renewal

11.1	This Agreement shall be effective as of the date the Wireless CLEC executes Schedule “A” forming part of this Agreement, and shall expire on April 1, 2008.

11.2	The term of this agreement shall be automatically renewed for successive periods of five  (5) years after the initial term, as stipulated in Article 11.1.

11.3	The term of this Agreement and any renewal term shall be in force unless one party gives to the other at least six (6) months’ written notice of termination prior to the end of the said term.

11.4	Notwithstanding Article 11.1, this Agreement shall automatically terminate on the same date as:

- The E9-1-1 Service Provider ceases to provide an E 9-1-1 emergency calling service to the Municipality, or,

- The Wireless CLEC ceases to employ the E9-1-1 facilities of the E-9-1-1 Service Provider, in that it will provide its own E9-1-1 Emergency Calling Service.

12.	Force Majeure

12.1	Neither the Wireless CLEC nor the Municipality will be held responsible for any damages or delays as a result of war, invasion, insurrection, demonstrations, or as a result of decisions by civilian or military authorities, fire, floods, strikes, decisions or regulatory authorities, and, generally, as a result of any event that is beyond the Municipality’s or the Wireless CLEC’s reasonable control.

12.2	In the event of a disaster or force majeure, the Wireless CLEC and the Municipality will cooperate and make all reasonable efforts to provide temporary replacement service until permanent service is completely restored.

12.3	The Municipality may designate a back up Call Answer Centre to which E9-1-1 calls will be directed in the event that the primary PSAP is unable to accept the calls, for any reason.

12.4	The costs required to provide temporary replacement service will be borne according to the sharing of obligations between the Wireless CLEC and the Municipality, as indicated in Article 4 of this Agreement.

13.	Waiver

The failure of either party to require the performance of any obligation hereunder, or the waiver of any obligation in a specific instance, will not be interpreted as a general waiver of any of the obligations, hereunder, which will continue to remain in full force and effect.

14.	Relationship to the Parties

This Agreement will not create nor will it be interpreted as creating any association, partnership, any employment relationship or any agency relationship between the parties.

15.	Entire Agreement

15.1	Except as otherwise stated herein, this Agreement constitutes the entire agreement of the parties and supersedes any previous agreement, whether written or verbal.  Should any provision of this Agreement be declared null, void or inoperative, the remainder of the Agreement will remain in full force and effect.

15.2	The parties agree that Articles 1,6,10,12,14,15,16 and 17 of this Agreement shall survive and remain in force notwithstanding the expiration or termination of this Agreement.

15.3	It is expressly understood that this Agreement and E9-1-1 Emergency Calling Service are subject to such terms and conditions as the CRTC or its successors may impose from time to time.

16.	Arbitration Clause

Except with respect to any matter within the jurisdiction of the Commission, any dispute or disagreement that may occur pursuant to this Agreement will be settled in a binding manner by way of arbitration in accordance with the Arbitration Act, 1991 (Ontario), as amended.  Each party will bear its own costs of arbitration.  All decisions of the arbitrator(s) are fully binding and enforceable upon the parties.

17.	Notices

Any notice required pursuant to this Agreement shall be in writing and delivered personally, by courier, or sent by registered mail (with proper postage), to, in the case of notice to the Municipality, the address listed on this page, and in the case of the Wireless CLEC, the address listed in Schedule “A”, or to such other address as either party may indicate to the other.  In the event of a strike or other disruption of postal service, or an anticipated strike or disruption, delivery either personally or by courier only, will be effective.

Notice to the Municipality:

_______________________

_______________________

_______________________

_______________________

18.	 Applicable Law

This Agreement shall be governed by the laws of the Province of Ontario and Canada.

SIGNED, SEALED AND DELIVERED

THE MUNICIPALITY

Per: __________________________________

Per: __________________________________(c/s)

Dated: ________________________________

SCHEDULE “A”

Wireless CLEC Adherence Schedule

- This Schedule “A” forms part of an Agreement for the Provision of E9-1-1 Emergency Calling Service in the Province of Ontario - For Use by Wireless Competitive Local Exchange Carriers (the “Agreement”) between ____________________________ (“Municipality”), having executed the Agreement on _________________________, and the Wireless Competitive Local Exchange Carrier (the “Wireless CLEC”) identified below, having executed this Schedule “A” on ____________________________.

- Upon execution of this Schedule “A” and its delivery to the Municipality pursuant to the provisions of Article 17 of the Agreement, the Wireless CLEC agrees that it will be bound to the terms and conditions of the Agreement as if it had executed the Agreement directly.

- Pursuant to Article 17 of the Agreement, the Wireless CLEC’s address for notices is:

_______________________

_______________________

_______________________

_______________________

SIGNED, SEALED AND DELIVERED

WIRELESS CLEC:	__________________________________

Per: __________________________________

Per: __________________________________(c/s)

(I have the authority to bind the corporation)

SCHEDULE “B”

Location of PSAP and ERA’s

PSAP

Contact _____________________________________________________

Address _____________________________________________________

Phone _(_____)________________

Fax ___(_____)________________

Back-up PSAP

Contact ______________________________________________________

Address ______________________________________________________

Phone _(_____)_______________

Fax ___(_____)_______________

Fire: ERA Detail per Schedule D

Ambulance: ERA Detail per Schedule D

Police: ERA Detail per Schedule D

Municipal: Detail per Schedule C

SCHEDULE “C”

Municipal Contacts

911 Contact Information:

Main Municipal Contact: _____________________________________________

Address:

Street:              ______________________________________________________

Town/City       ______________________________________________________

Postal Code     _______________

Phone: _(______)________________

Fax: ___(______)________________

Municipal Address Co-ordinator: _______________________________________

Address:

Street:               ______________________________________________________

Town/City:       ______________________________________________________

Postal Code:     _________________

Phone: __(_____)__________________

Fax: ____(_____)__________________

SCHEDULE “D”

Serving Areas and Emergency Service Zones

Per attached Service Address Control Group documents.